## Slide 1
PHOTON
A Dynamically Reconfigurable Hybrid
Nano-photonic-Electric Network-on-Chip Shirish Bahirat Sudeep Pasricha
{shirish.bahirat@colostate.edu} {sudeep@colostate.edu}
Colorado State University

## Slide 2
Chip Multi Processors (CMPs)
IP
I/O
Memory
Hard Disk
Single Core
IP
I/O
Memory
Hard Disk
IP
IP
Bus
Multi-Core
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
Networks On Chip
Increasing application complexity
  Parallel processing
Bus based architecture does not scale
  High Latency, Low Bandwidth, Low Predictability
Networks-on-chip (NoCs) enable multi-core systems
  Better Bandwidth, Scalability and reliability

## Slide 3
On Chip Interconnect Challenges
key challenge: Communication
  Scalability
  Performance
  Power
NoC helps! However
  High latency
  High Power Dissipation
  ~40% of overall power in MIT RAW
  ~30% of overall power in Intel 80 core teraflop chip
  Temperature, chip reliability etc

## Slide 4
Contribution
Photonic ring interfaced with 2D electrical mesh
Key enabler: CMOS ICs with 3D integration
Separate photonic and logic layers
Propose novel hybrid nanophotonic-electric architecture called PHOTON
  Low Latency, High Bandwidth, Low Power

## Slide 5
Components Photonic Interconnect
Laser light source: multi-wavelength mode-locked
Modulator: microring-resonator structure
Detector: SiGe photodetector w/ microring resonator filters
Waveguide: high refractive index Silicon On Insulator (SOI)
  WDM: Wave Length Division Multiplexing
  n interfacing cores having exclusive access to λ/n wavelengths

## Slide 6
Components of Photonic Ring
Microring resonators as couplers
Destructive overlap with older messages in ring
  Attenuators before each modulator
    Sink for corresponding wavelength if signal goes full circle

## Slide 7
Photonic Region of Influence (PRI)
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
IP
IP
R
R
R
R
R
R
R
R
IP
IP
IP
IP
R
R
R
R
IP
R
R
IP
R
R
R
R
IP
R
R
G
G
G
G
PRI SIZE = 4
PRI SIZE = 1
PRI SIZE = 6
PRI SIZE = 3
Number of cores around gateway utilizing photonic path

## Slide 8
  6-tuple <k,b,n,r,w,c> Paramerization
    k: Number of photonic rings
    b: Bitwidth of the waveguides
    n: Number of gateway interfaces
    r: PRI size
    w: Number of WDM channels
    c: Number of cores in the CMP
PHOTON Multi Ring Topology
k=4,b=256, n=16,r=2,w=16,c=36
k=5,b=256, n=16,r=2,w=16,c=36
k=3,b=256, n=12,r=2,w=16,c=36

## Slide 9
System Level Architecture
Electrical Mesh
  Wormhole switching
  Flit width of 256
  Regular 2D electrical mesh topology
  Input queued crossbar, with 4-flit buffer at ports
  Enhanced XY dimension order routing
Photonic ring
  Parallel waveguides = flit width = 256
  Gateway interface routers enable inter-layer transfers
    Reduces router overhead
ACK/NACK flow control
  If multiple requests contend for access to the photonic waveguide at a gateway interface, then the request with the furthest distance given priority

## Slide 10
PRI Aware X-Y Router
Optical
Optical
WDM Control
Input Ports
Output Ports
Photonic layer
Timeout Monitor
Routing and Switch Allocation
Region Validation
Arbitration
n-k regular routers w/ region validation, timeout monitor
Enhanced gateway interface
  add < 1% area overhead (minimal)
Data
Data
N
W
E
S
Local
N
W
E
S
Local
6x6 Crossbar
Switch
Flow Ctrl
Flow Ctrl

## Slide 11
PRI Aware X-Y Routing
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
IP
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
IP
IP
R
R
R
R
R
R
R
R
IP
IP
IP
IP
R
R
R
R
IP
R
R
IP
R
R
R
R
IP
R
R
G
G
G
G
PRI SIZE = 4
PRI SIZE = 1
PRI SIZE = 6
PRI SIZE = 3
Non PRI transfers
Inter PRI transfers
Intra PRI transfers

## Slide 12
Dynamic Reconfiguration
PRI:
  Small PRI promotes transfer over electrical NoC
  Large PRI promotes transfers over photonic rings
WDM:
  Dissipated power in the modulators and receivers
  Reducing number of WDM channels can save power
DVS/DFS:
  Dynamic supply and voltage clock scaling is one of the most widely used runtime optimization
  Performance requirements can lead to almost quadratic reduction in power

## Slide 13
Experimental SetUp
Goal:
  Analyze power, latency and performance tradeoffs as compared
    Traditional NoC architectures
    Non reconfigurable hybrid photonic NoC
    Other hybrid photonic NoCs proposed in recent literature
Simulation parameters:
  CMP/NoC Sizes: 6x6, 10x10
  Benchmarks: Splash 2
  Runtime Dynamic Configuration
Simulation methodology:
  SystemC: Allows hardware and software components
  Cycle accurate model

## Slide 14
Assumptions
Loss | 
Coupler/Splitter Optical Loss | 1.2 dB
Non Linearity Optical Loss | 1 dB at 30 mW
Waveguide Crossing Loss | 0.05 dB
Ring modulator loss | 1 dB
Receiver Filter Loss | 1.5 dB
Photo detector Loss | 0.1 dB
SOI Waveguide Loss | 3 dB/cm
Delay | 
Electrical delay | 42 ps/mm
Electrical laser power | 3.3 W with 30% η
Modulator Driver Delay | 9.5 ps
Modulator Delay | 3.1 ps
Waveguide Delay | 15.4 ps/mm
Photo Detector Delay | 0.22 ps
Receiver Delay | 24.0 ps
Power | 
Data Traffic Dependent Energy Modulator and Receiver | 20 fJ/bit
Static Energy (clock, leakage) | 5 fJ/bit
Thermal tuning energy (20K Temperature range) 1 heater per micro ring resonator | 16 fJ/bit/heater
Bitwidth of the waveguides | 256
Electrical laser power | 3.3 W with 30% η
CMOS | 32 nm
Based on real world Data and ITRS projections

## Slide 15
Dynamic Reconfiguration Improvement
Improvement compared non dynamic
Greater number of photonic rings: more opportunities for fine tuning traffic distribution

## Slide 16
Improvement compared to Electrical Mesh
Significant improvement for relatively smaller complexity
Power Improvement

## Slide 17
Improvement Compared to Electrical Mesh
PHOTON energy-delay improvements relative to the electrical mesh
150× energy-delay product improvement for medium sized (36 core) NoCs.
74× improvement for large sized (100 core) NoCs

## Slide 18
Improvement compared to Photonic Torus
PHOTON has significant advantage over more complex hybrid photonic torus architecture
  Fewer power hungry photonic components
  Aggressive power savings with runtime reconfiguration

## Slide 19
Area Overhead
Hybrid photonic torus has 10-15× more photonic layer area
About 1.5-2× electrical layer area overhead
Electrical layer overhead for PHOTON is minimal
Optical Layer area improvement
Silicon layer overhead

## Slide 20
Conclusion
Future CMPs with hundreds of cores
  Require a scalable communication fabric
  Reducing power consumption is essential
  High performance per watt
2D electrical NoCs unable to meet these requirements
Proposed novel PHOTON shows significant promise
  Simpler and scalable architecture
  Lower area overhead
  Significant power and performance gains

## Slide 21
Thank You
.
Questions
Discussion